## Slide 1: Prosjektoppdatering
15.10.2024

## Slide 2: Updated Randles circuit
Two Randles Circuits in series on the form:
Z = R_el + Z(L) + Z1 + Z2
  (Z2 without Warburg)
  Non-ideal capacitance (CPE) and warburg with alpha parameter
  Best error I get (with scipy.minimize) is ca. 3.3e-7

## Slide 3: Optimized ECM parameters: estimation for simulation parameters
Negative/Positive electrode double-layer capacity [F.m-2]: CPE/area(electrode)
  Area(electrode) = Electrode height [m]*Electrode width [m]
  Negative: CPE = Q2
  Positive: CPE = Q1
Negative/Positive electrode exchange-current density [A.m-2]: i0 = (R*T)/(n*F*resistance(electrode))
  (from small overpotentials and assuming a symmetrical charge transfer process)
  Negative: resistance(electrode) = R_ct2
  Positive: resistance(electrode) = R_ct1
Electrolyte conductivity [S.m-1]: 1/(thickness(separator)*resistance(electrolyte))
Negative/Positive electrode conductivity [S.m-1]: thickness(electrode)/(resistance(electrode)*area(electrode))
  Negative: resistance(electrode) = R_ct2, thickness(electrode) = anode_thick,
  Positive: resistance(electrode) = R_ct1, thickness(electrode) = cathode_thick
Electrolyte/Positive particle/Negative particle diffusivity [m2.s-1]: ((R*T)/(n*F*area*A))^2
  Negative: area = e_height*anode_thick, A = A2?
  Positive: area = e_height*cathode_thick, A = A1
  Electrolyte: area = e_height*s_thick, A = A2?

## Slide 4
Have I described the electrolyte diffusivity correctly?
  - Why A2 in electrolyte to get a meaningful result for example?